PHYSICS 4A EXAM 5

December 6, 2002

Name:____________________

Rules for Exam:

- Only Scientific Calculators are allowed!

- Show your work on non-multiple choice problems. NO WORK=NO CREDIT.

- Include units with each answer. One point deduction per infraction.

- Round off to 2 decimal places and circle your final answers.

- Circle your final answers.

Good Luck!

| Scores |  |
| --- | --- |
| Prob 1 (20 pts) |  |
| Prob 2 (10 pts) |  |
| Prob 3-5 (13pts) |  |
| Prob 6 (20pts) |  |
| Prob 7 (20 pts) |  |
| Prob 8 (15 pts) |  |
| TOTAL (98 max) |  |
| % (out of 98) |  |

PROBLEMS

- A cable attached to a 4.80 m rod that can pivot at its base supports a 10,600 N shark. (Neglect the weight of the rod.) Calculate the tension in the tie-rope between the wall and the rod and the horizontal force exerted on the base of the rod if the system is in the position shown. Don’t forget to include a free-body diagram in your solution (20 points).

T=5380N

R=5060N

- An 18ft plank is supported on two rocks 6ft and 2ft from opposite ends. The plank weighs 100 lbs. How far can a 150lb a man walk to the right before the plank tips up and hits him. What are the forces at A and B when the plank begins to tip (10 points)

X=2ft

Fb=250lb

Fa=0

- Complete the following statement: In general, the term stress refers to (4 points)

- a change in volume.

- a change in length.

- a force per unit area.

- a fractional change in length.

- a force per unit length.

- An aluminum wire and steel wire of the same length and diameter are joined to form a wire twice their original length. The wire is fastened to the roof and a weight W is attached to the other end. Neglecting the mass of the wires, which of the following is true (4 points)?

- The aluminum portion of the wire will stretch by the same amount as the steel wire.

- The tensions in both portions of the wire are the same.

- None of the above statements is true.

- Consider a hypothetical planet in our solar system whose average distance from the Sun is about four times that of Earth.  Determine the orbital period for this hypothetical planet (5 points).

- 0.25 year

- 2.5 years

- 4 years

- 8 years

- 16 years

C,B,D

- Calculate the gravitational field of a solid sphere of density (r)=Cr, mass M and radius R at points r1<R and r2>R. Sketch a graph of the magnitude of the gravitational field as a function of r, the distance from the center of the sphere. Don’t forget to determine the value of the constant C. (20 points).

C=M/R4

g=GM/r22 in r direction outside sphere

g=GMr12/R24 in r direction outside sphere

The graph should be obvious

- A rocket is fired at 36.9° to the local vertical with an initial speed v0 = (GM/R)1/2 , where M is the mass of the earth and R is its radius.  What is its maximum distance from the earth’s center? You may neglect air friction and the Earth’s rotation. You must show all your work (20 points).

r=1.8RE

- A 600kg satellite orbits the Earth at a constant altitude of 200km. How much energy must be added to the system to move the satellite into a circular orbit with altitude 400km? (15 points).

# Text boxes

R

r1

r2

(

v0

rmax

### A

### B

### 6ft

### 2ft