Physics 4A

Measurement Worksheet

Introduction:  This preliminary exercise (Individualized, No Lab Partners) is designed to provide a "hands-on" review of measurement, which will include: some familiar or unfamiliar instruments, some SI units, the measuring process, significant figures, derived quantites, and graphing.  Before beginning this important exercise, please read the "Significant Figures", "Graphical Analysis Handout", “The Lab Manual Handout”, and “The Vernier & Micrometer” handouts.

Part 1: Measurement & SI Units

Directions:  Measure the following quantities and report them in the indicated units.  Be sure to report the correct number of significant figures.

d = 	    ____________  cm

- During the semester, you will be using verniers calipers to measuring objects in centimeters (cm). Record the caliper reading shown below (Each small division on the scale below is one mm.) When you use the vernier calipers in the lab, make sure you read the correct scale since some of the calipers have both inch and centimeter scales.

- __________ cm

- __________ cm

- __________ cm

- Obtain three wires. Use a Micrometer to measure their

Diameter (indicate color of wire):

a.  __________	 mm	b.  __________ mm	c. __________	 mm

D.  Obtain a sheet of white copy paper and measure its

a. length : 	__________ cm           b. width:  	__________ cm

c. thickness:   __________ cm  	d. mass:  __________ g

E.  Measure Room

Temperature: __________  deg C

F.  Measure ( by rolling a cylinder out on a piece of paper. Use a Vernier caliper to measure d.

C =  __________ 		d =  __________

(  =  __________ 	% Error =  __________

F.  Determine the density of H2O.

Mass of Graduate:  __________	Mass of Graduate + H2O:   __________

Mass of H2O:  __________           Volume of H2O: __________   Density: __________

Part 2: Significant Figures & Derived Quantities

Directions:  Carry out the indicated operations below and report the answer to the correct number of significant figures in the space provided.

1.  	__________	2.  __________

3.    __________	4.   __________

5.   __________	6.  __________

7.  0.011 has 	__________    sig. figs	8. 64,340 has  __________     sig. figs

- Write 57,440 to 4 sig. figs using scientific notation:   __________

- Calculate the average of the following measurements (don’t forget to apply the rules for sig figs): 2.06cm, 2.18cm, 2.05cm, 2.10cm, 2.11cm, 2.09cm.  __________

Express your answers to the following in scientific notation:

11.  Add 5.80 x 103 and 6.75 x 102  =  	__________

12.  Multiply 6.687 x 10-3 and 479 x 10-4 =   _________

13.  Divide 1398 x 10-4 by 8.8469 x 10-3 =   __________

Part 3: Graphing

| Penny | Penny Mass (g) |
| --- | --- |

- Obtain the beaker of pennies, place one on the centigram balance, and measure its mass in grams.  Record this mass in a data table made on a separate piece of paper.  Now add a penny and measure the mass of both pennies and record in your table.  Continue adding pennies, and measuring and recording the total mass for a total of at least fifteen pennies.  Now plot a graph of mass vs. number of pennies and evaluate the slope (show your calculation below your data table).

| Number of Pennies | Mass of Pennies (g) |
| --- | --- |

# Does your slope have units? Explain.  ____________________________________

What does the slope mean?  __________________________________

Be sure to attach your data table and graph to this worksheet.

What is the slope of your graph to the correct number of decimal places?____________

- Weigh each of the pennies individually and list their masses in a table.

Calculate their average mass.		_____________________

How does this compare to the slope of the graph? Why? ________________________________________________________________________

Calculate the standard deviation from the mean. _____________________

(always keep one sig. fig.)

Calculate the precision the mean .		          _____________________

(always keep one sig. fig.)

What is the precision of the balance?		    _____________________

# (always keep one sig. fig.)

What does the standard deviation of the mean tell you?

How does the precision of the mean compare to the precision of the balance? Should they be the same in this experiment? Why or Why not?

Part 4 Propagation of Errors

Measure the diameter of the given sphere with the Vernier caliper. 		D=__________cm

What is precision of your Vernier caliper?				           D=__________cm

Using your knowledge of differential calculus (refer to your calculus textbook), estimate the error in the volume of the sphere. Show your work below.  				V=__________cm3

Use a Vernier caliper to measure the block’s length, L, width, W, and height, H, five times. Make sure you use different locations on the block when you repeat each measurement. Then calculate the average length, width, and height along with their uncertainties. Report values using the format L(L, W(W, and H(H. Finally calculate the average volume of the block along with its uncertainty (using the proper method to propagate the errors).

| Trial Number | Length(cm) | Width(cm) | Height (cm) |
| --- | --- | --- | --- |
| 1 |  |  |  |
| 2 |  |  |  |
| 3 |  |  |  |
| 4 |  |  |  |
| 5 |  |  |  |

Average Length      = 	___________cm

Average Width        =  	___________cm

Average Height      = 	___________cm

(Lavg ) (Wavg ) (Havg )= 	___________cm3 = ______________m3