Conceptual Questions: DC Circuits

- Suppose a potential difference is applied to a conductor that obeys Ohm’s Law. Now suppose we double the potential difference across the conductor. Which of the following statements is true about the conductor?

  - Its resistance doubles.

  - The current through it doubles.

  - The resistance drops by a factor of two.

  - The power dissipated by the conductor doubles.

- The transistor circuit below is to be checked for proper operation.  According to specifications, point C should be at +15.0V with respect to ground. If this is true what is the voltage at point D? (Hint- the role of the transistor is not important in this question; assume the capacitors are fully charged).

- 3.0V

- 5.0V

- 9.0V

- 10.0V

- What is the potential difference across the 1f capacitor at the bottom of the diagram is in the transistor circuit.

  - 0.0V

  - 3.0V

  - 5.0V

  - 9.0V

  - 10.0V

- What is the current between points C and D of the transistor circuit?

  - 1.7A

  - 2.5A

  - 5.0A

  - 9.0A

- Two cylindrical copper wires have the same mass. Wire A is three times as long as wire B. Their resistances are related by

  - RA=27RB

  - RA=9RB

  - RA=3RB

  - RA=RB

- Two resistors dissipate the same amount of power. The potential drop across resistor A is twice that across resistor B. If the resistance of B is R, what is the resistance of A?

  - R

  - 2R

  - R/2

  - 4R

  - R/4

In questions 7-10:

a) bulbs are identical

b) treat the bulbs as ohmic resistors

c) treat the wires as zero resistance connectors

d) batteries are ideal (no internal resistance)

- In which case is the bulb labeled “1” brightest?

- In which case is the bulb labeled “1” brightest?

- In which case is current through the ammeter greatest? Ties are possible. If ties exist please indicate them.

- In which case is the current through the ammeter greatest? Ties are possible. If ties exist please indicate them.

- True or False: The equivalent resistance of a network of three parallel resistors is always less than that of the smallest resistance in the network.

- Which has a larger resistance, a 100W lamp, or a 60W lamp?__________

Refer to the circuit shown below. Positive terminal of battery is shown.

- All lamps (circles) are identical. Which lamp(s) burn(s) brighter?

a.  A		b.  B		c.   C		d.  C and D

e.  A and B

- The larger current is through lamp

a.  A 		b.  B

c.  current is same through A and C

d. current is same through C and D

- If lamp A only is unscrewed, which lamp(s) will go out?

a.  B		b.  C		c.  B and C		d.  none of the others

- If lamp C only is unscrewed, which lamp(s) will go out?

a.  A only		b.  B only		c.   D only		d.  A,B and D			e.  A and D only

- In the circuit shown, the larger voltage is across							a.  A	b.  C	c.  voltage is same across A & C 	d. voltage is same across C & D

- In the circuit shown, the larger current is through lamp

a.  C		b.  D		c.  current is same through C and D

- If a wire were connected from point 1 to point 2 in the circuit, which lamps would burn?

a.  A		b.  B		c.  A and B	d.  all		e.  C and D

# Text boxes

B

C

A

Battery

D

E

B

Transistor

D

C

2

1