#### EXAM 4

May 19, 2004

Name:____________________

Rules for Exam:

- Calculators are allowed, but you may not share one.

- Show your work on non-multiple choice problems. NO WORK=NO CREDIT.

- Include units with each answer. One point deduction per infraction.

- Points will be deducted for students that refuse to turn in their exams, when asked to do so (at the end of class).

- Round off to 2 decimal places and circle your final answers.

- Circle your final answers.

Good Luck!

| Scores |  |
| --- | --- |
| Part 1 (16 pts) |  |
| Problem 1 (10 pts) |  |
| Problem 2 (14 pts) |  |
| Problem 3 (30 pts) |  |
| Problem 4 (20 pts) |  |
| Problem 5 (15 pts) |  |
| TOTAL (105 max) |  |
| % (out of 100) |  |

Multiple choice and short answer questions (4 points each, unless noted)

- The light bulb has a resistance R, and the emf drives the circuit with a frequency f. The light bulb glows most brightly at

- very low frequencies

- very high frequencies

- the frequency f=2/(LC)1/2

- Which condition of motion must be met with regard to a charged particle if it is in the process of emitting electromagnetic radiation?

- It moves with constant velocity.

- It accelerates.

- It moves at the speed of light.

- It moves parallel to a uniform magnetic field

- When the current through an inductor doubles the energy stored by the magnetic field

- increases by a factor of 4.

- decreases by a factor of 4.

- increases by a factor of 2.

- decreases by a factor of 2.

- Two current carrying coils of wire are close to each other. We can change the mutual inductance of the pair by

- changing the relative positions of the coils.

- changing the currents in the coils.

- increasing the number of turns in one of the coils.

- Both A and B are correct.

- Both A and C are correct.

- A, B, and C are correct.

B,B,A,E

Name:_____________________________________________

PROBLEMS

- At a distance of 40km from a radio transmitter, the amplitude of the E-field is 0.70V/m. What is the total power emitted by the radio transmitter if the electromagnetic waves are emitted uniformly in all directions? (10 points)

1.31x107W

- Write out the formulas for the electric and magnetic fields for an electromagnetic plane wave with the following characteristics. The wave is traveling in the negative x-direction with a frequency of 100Mhz and the electric field of magnitude Eo is perpendicular to the z-direction (don’t forget to calculate its wavelength). Why would the Poynting vector be useful in the solving this problem (14 points)?

=3m

- In the circuit shown below, the L=0.250H, C=10F, R=470and E =141in377t.

  - What is the impedance and the phase angle of the circuit (10 points)?

500



  - What is the rms voltage between A and B (5 points)?

34V

  - What is the resonance frequency of the circuit (5 points)?

101Hz

  - Draw an accurate phasor diagram at t=0.0167s (10 points).

- A 2000 resistor and a 1.0F capacitor are connected in series across a 120V (rms) 60Hz line.

- What is the rms value of the current (5 points)?

0.036A

- What is the average power dissipated in the circuit (5 points)?

2.6W

- What will be the reading of an AC voltmeter connected across the capacitor (5 points)?

95V

Name:_____________________________________________

- In the circuit shown, the 10-volt battery has negligible internal resistance. The switch is closed for a long period of time, and then opened.  Calculate the potential at points A and B (with respect to ground) when the switch is opened, and 1.0 milliseconds after the switch is opened (15 points).

VA=-30V; VB=10V

NOTE:∆VBA=VB-VA=+40V

VA=-4.1V

VB=1.4V

# Text boxes

E

C

L

E

L

C

R

A

B

50

150

0.1H

10V

#### A

#### B