Name_________________

Capacitor Worksheet

The following assignment is due at the beginning of our next lecture.

A parallel plate capacitor consists of two large plates of area A and separation d.  Assume the plates are charged and the battery is disconnected from it. Suppose a thin metal plate of area A is inserted halfway between the two plates.

How is the electric field affected after the plate is inserted?

Use the grid below to sketch the magnitudes of the electric field and electric potential between the plates after the plate is inserted.

How is the total capacitance affected? Compare its value to that of the original capacitor.

Suppose the plate that is inserted has a finite thickness, t. How is the electric field affected

Use the grid below to sketch the magnitudes of the electric field and electric potential between the plates after the plate of thickness, t, is inserted.

How is the total capacitance affected? Compare its value to that of the original capacitor.

# Text boxes

d

d

d

Before

# After

t