Name_________________

Motional EMF Worksheet

The following assignment is due at the beginning of our next lecture.

- The figure shows a uniform, 3.0-T magnetic field that is normal to the plane of a conducting, circular loop with a resistance of 1.5  and a radius of 0.024 m.  The magnetic field is directed out of the paper as shown.

- What is the magnitude of the average induced emf in the loop if the magnitude of the magnetic field is doubled in 0.4 s?

- What is the average current around the loop if the magnitude of the magnetic field is doubled in 0.4 s? Make sure you specify the direction of the current.

- What is the power (the rate in which energy) is dissipated in the loop?

- What would be the direction of the induced current if the magnetic field was held constant and the loop is pulled out of the region that contains the field?