PHYSICS A

EXAM 4

### April 28, 2000

### Name:___________________SSN:______________

Rules for Exam:

1.	Crib sheet will be provided by instructor.

2.	Calculators are allowed, but you may not share one.

3. 	Show your work on numerical problems. Do not expect any credit for a problem if I cannot logically follow what you have put on your paper.

- Follow the rules for significant figures. One point will be deducted for each infraction.

- Make sure you include units with each answer. One point will be deducted for each infraction.

- Points will be deducted for students that refuse to turn in their exams, when asked to do so (at the end of class).

- Circle your final answers.

________________________________________________________

Conversion Factors:

1 mile= 5280 feet (exact)		1 day= 24 hours (exact)

1 km =0.6214 miles			1 year=365.25 days

1 mile= 1609.3 m			1 atm=14.7psi=1.013x105 Pa=1.013x105 N/m2

1 m=39.37 inches			1 cm= 10 mm (exact)

k=9.0x109 N-m2/C2			1hr=60 minutes=3600 seconds (exact)

Acceleration due to gravity =9.80m/s2 =32.2ft/s2 downward

|  | SCORE |
| --- | --- |
| PROBLEM 1 (10points) |  |
| PROBLEM 2 (6 points) |  |
| PROBLEM 3 (19 points) |  |
| PROBLEM 4 (20 points) |  |
| PROBLEM 5 (30 points) |  |
| TOTAL (85 max) |  |
| Percentage out of 85 points |  |

Solve the problems you think are easiest first.

Name:_____________________________________________

- How long would it take a 4.50x103 Watt motor to raise a 175-kg boiler to a platform 15.0-m above the floor? (10 points) Watch your significant figures.

##### Ans 5.71s

- A gardener pushes a mower a distance of 25.0m in mowing a yard. The handle of the mower makes an angle of 60.0-degrees with the ground. The gardener exerts a force of 36.0N along the handle of the mower. How much work does the gardener do in mowing the lawn? (6 points)

Ans 4.50x102J

Name:_____________________________________________

- A 28-kg sled is pulled up a frictionless hill. The angle of the hill with respect to the horizontal is 12.0º.  The applied force is parallel to the direction of its displacement. Draw a picture for your benefit. Keep your final answers to 2 significant figures!

- How much work is done by gravity if the sled is pushed a distance of 3.2-m? (5 points)

Ans -1.8x102J

- What is its change in potential energy after it has traveled 3.2-m? (5 points)

Ans +1.8x102J

- Calculate the magnitude of the force acting on the sled if the velocity of the box is constant over the 3.2-m distance it travels? What is the concept that must be applied to solve this problem? (9 points)

##### Ans 57N

Name:_____________________________________________

- A cat burglar is making an escape by sliding down the cables as shown below. The mass of the burglar is 92.0 kg. Keep your final answers to 3 significant figures!

- Draw a free-body diagram indicating all the forces acting on the cat burglar. Make sure you also show the components of all forces. (8 points)

##### Ans  see instructor

- Find the tension (T1 and T2) in both cables. (12 points)

Ans 1.32x103N and 967N

Name:_____________________________________________

- A block is pulled by the forces shown below. The surface is frictionless.

- Draw a free-body diagram indicating all the forces acting on the block. Indicate each component of each force. (10 points)

##### Ans see instructor

- Calculate the normal force acting on the object? (8 points)

##### Ans 1.30N

- Calculate the net (unbalanced force) acting on the object in the horizontal direction. (6 points)

##### Ans 3.07N

- What is the acceleration of the block? Which law are you using for this calculation (6 points)?

Ans 0.842m/s2 to right

# Text boxes

#### P=45.0 N

#### F=32.0 N

#### 3.65kg